## Slide 1
Start up
Anderson Smartmix TMR
2017
A280/380/
520/700/950/
1230

## Slide 2
Product presentation
The SMARTMIX machine is a trailed machine designed for feeding herds.
It provides :
. Storage of silage, complements and all types of straw, hay and wrapped bales.
. Mixing and, if necessary, cutting these different products.
. Transport of loaded products to the distribution site.
. The distribution of loaded products.
. Straw distribution for a herd's litter

## Slide 3
Smartmix Start-up
Couple the machine to the tractor. Make sure the tank is horizontal on a flat ground.
Connect hydraulic source to the machine (1 in and 1 out).
Connect electric cables for controls and road lights.
Place the leg support in its transport position.
Connect the transmission shaft (PTO) to the machine.
Mount the electrical control box it in the cab. It will be held in place by its metal clip. It must be positioned in the cab so as to :
  Be in the best position for controlling the machine from the tractor seat.
  Avoid impeding the other tractor controls.
Test the Smart Controller and set the recipes at the same time.

## Slide 4
Hydraulic brake connector
Electric fitting
Power take-off
540 and 1000 rpm
Eye bolt coupling
Tractor fittings
*Hydraulic source :
- Direct control version (tractor distribution) :
Two double-acting hydraulic distributors (4 female 1/2" clack valves) for Smartmix with conveyor.
One double-acting hydraulic distributors (2 female 1/2" clack valves) for Smartmix direct distribution or Jet.
- Electrical control version :
A single-acting hydraulic distributor (+ return) or a double-acting one (two female ½ clack valves).
Distributor maintained in continuous pumping.
Direct return to the tank recommended so as to reduce oil heating.
For self-regulating pumps, compulsory return to the bowl.
* Nominal flow rate :
- Direct control version : 25 - 40 l/min (40 - 60 l/min with elevator conveyor)
- Electrical control version : 30 – 90 l/min

## Slide 5
The SMARTMIX coupling ring is set to standard for a 450 mm tractor coupling (size A) on Smartrmix AXXX to AXXX Direct Trap, and 550 mm on the other Smartmix machines.
Do the measures on a flat and horizontal ground, the machine must be empty, uncoupled with the parking brake on.
If the difference between size A and B (tank horizontal) is greater than 50 mm, you can adjust the height of your SMARTMIX coupling.
*To adjust the height of the SMARTMIX coupling, refer to the instruction manual.
Coupling position

## Slide 6
Smart Control
Description
Smart Control is a device for the integrated management of the hydraulic and weighing functions.
Features & Advantages
Portable device ;
Internal battery rechargeable;
Functions management: settings, parameter status, warning and alarms;
Easy and immediate settings, working data’s stored and exported through a dedicated USB port;
Wireless connection;
Highly customizable both in terms of functions and graphic design to fit every customer’s needs;
User friendly device with soft keys and icons that identify each function;
Safety alarms settings;
Color Display for high visibility;
Waterproof
Great flexibility during loading and feed out

## Slide 7
Smart Control
Smart Control offers:
Three working modes:
Weighing
Hydraulic
Combined (weighing and hydraulic)
Programmable weighing system with:
99 recipes (max 24 components)
48 distribution programs (48 distribution points/pens each)
Choice of components from a list of 99
Choice of distribution points from a list of 64
DTM Suite feeding management software compatibility
Service menu with working hours counter and overload counter
Internal diagnostic

## Slide 8
The Smart controller is associate with a Smart box located on the spirmix.
Smart Control

## Slide 9
Smart Control keyboard
1. ON/OFF key on the right side.
2. Function and setting keys.
3. ENTER key.
4. Key for change the working mode.
5. Directional keys.
6. RESET key.
7. Display.
8. STOP key.

## Slide 10
Setting of the parameters
1- Turn on the Smart Control device pressing the ON/OFF key.
2- Press the CONFIG key (F11).

## Slide 11
Setting of the parameters
3- Press the “Password menu” key (F4) in order to set the password.
4- Enter the number of the password with the function keys and press the ENTER key.

## Slide 12
Setting of the parameters
LIST OF PASSWORDS THAT CAN BE SELECTED
12 Calibration
99 Setting of the maximum weight (over-range)
454 Setting of kg / pounds
700 Choice of communication mode (RF via Xbee or serial via cable)
789 Deleting of load/unload program from external flash memory 790 Clearing of all components and unloading points
791 Loading of the names for default components and unloading points

## Slide 13
Setting of the parameters
Password 12: How to set the calibration value
1- From the modality Set password, select number 12 with the function keys.
2- Confirm with the ENTER key.
3- With the function keys change the value of this parameter if necessary.
4- Push the ENTER key to confirm the new calibration parameter. The indicator will return to Set password.
The calibration value depends on the number and capacity of the load cells. Contact dinamica generale® for further details. If a complete system has been bought, the DG indicators are already calibrated.

## Slide 14
Setting of the parameters
Password 99: How to set the Maximum weight
1- From the modality Set password, select number 99 with the function keys.
2- Confirm with the ENTER key.
3- With the function keys change the value* of this parameter if necessary, the range can be set at 100÷99999.
4- Push the ENTER key to confirm the new calibration parameter. The indicator will return to Set password.
*The value of this parameter is linked to the capacity of the machine, dinamica generale® suggests to set the maximum capacity of the machine.

## Slide 15
Setting of the parameters
Password 454: How to set the Maximum weight
1- From the modality Set password, select number 454 with the function keys.
2- Confirm with the ENTER key.
3- Selection of the unit of measure in kg or pounds with the function keys.
a) By setting 0=Kg the weight will be visualized in Kilograms.
b) By setting 1=Lb the weight will be visualized in Pounds.
4- Push the ENTER key to confirm the new calibration parameter. The indicator will return to Set password.

## Slide 16
Association to the smart box
1- Turn on the Smart Control device pressing the ON/OFF key.
2- Make sure that the devices are connected through cables.
3- Press the CONFIG key (F11).

## Slide 17
Association to the smart box
4- Press the “Pairing” key (F6) in order to associated the SMART Control to the SMART Box, then press the ENTER key.
5- The message of procedure complete appears with the serial number of device.
Restart the SMART Control after this operation.

## Slide 18
Use of the device
Weighing mode

## Slide 19
Use of the device
Weighing mode

## Slide 20
Use of the device
Weighing mode

## Slide 21
Use of the device
Weighing mode

## Slide 22
Use of the device
Weighing mode

## Slide 23
Anderson Smartmix TMR
Autumn 2016